Manchester Institute of Biotechnology  - Risk Assessment Form

| Date: 09/03/15 | Assessed by: Ron Burke | Validated by: Tanya Aspinall | Location: MIB G.063 | Review date: 08/03/16 |
| --- | --- | --- | --- | --- |

Task: Pipetting and dispensing of solutions using a Biomek FXp liquid handling station

| Activity | Hazard | Person(s) in danger | Existing measures to control risk | Risk rating | Result |
| --- | --- | --- | --- | --- | --- |
| Use of Machine | Mechanical | User | Automated, moving pipette heads present risk of injury, however the user is protected by a light curtain which halts all mechanical functions should the workstation be approached too closely | low | A |
| Pipetting and dispensing of solutions | chemical hazard | Staff | All staff must be trained by their supervisor or senior lab personnel in the safe method of pipetting and dispensing of solutions. A COSHH assessment (including information on what to do in case of accident) must be carried out for all chemicals and must be read and signed before the work begins. All identified control measures must be followed. The following items of PPE must be worn: Howie-style laboratory coat and BS EN374 compliant gloves (nitrile). Regular lab inspections monitor the wearing of PPE; users found not to be wearing PPE when the risk assessment states that it must be worn will be subject to the MIB compliance policy. All liquid handling functions must be checked weekly to ensure they are fully functional and correctly calibrated (carried out under software command). | low | A |

Authorisation by Facility Manager I confirm that I have considered and understand the experiment and the associated hazards. I am satisfied that all of the hazards have been identified and that the control measures to be followed will reduce the risks to acceptable levels. Print name: Signed: Date:

Declaration by researcher

I confirm that I have read this Risk Assessment and that I understand the hazards and risks involved and will follow all of the safety procedures stated.

Declaration by Facility manager

I confirm that the researcher who has signed below is competent to undertake the work. My counter-signature indicates that I am happy for the work to proceed.

| Name (please print) | signed | Facility manager countersignature | date |
| --- | --- | --- | --- |

Notes to accompany General Risk Assessment Form

This form must be completed for every experimental procedure conducted within the MIB.

The form must be signed by the researcher and their PI before the work starts.

- Date: Insert date that assessment form is completed.

- Assessed by: Insert the name of the assessor.

- Validated by: Insert the name of someone in a position to validate that the assessment has correctly identified hazards and addressed the risks (eg. the PI or an MIB H&S officer).

- Location: insert details of the exact location - floor and laboratory area.

- Review date: insert details of when the assessment will be reviewed as a matter of routine (maximum 1 year). ** The assessment must be reviewed if there are any significant changes to the work activity, the vicinity, the people exposed to the risk, etc.

- Task: insert a brief summary of the task.

- Activity: describe the activities involved in the task. Eg. use of gas cylinders, use of fume cupboard, use of computer or other electrical equipment, use of lab ovens, etc.

- Hazard: for each activity, list the hazards. Assessment of simple chemical risks (eg. use of cleaning chemicals in accordance with the instructions on the bottle) may be recorded here. More complex COSHH assessments, eg. for laboratory processes, should be recorded on the specific COSHH forms  and attached to this risk assessment form.

- Persons in danger: insert everyone who might be affected by the activity.  Remember those who are not immediately involved in the work, including cleaners, inexperienced lab workers, young persons on work experience, maintenance contractors, Estates personnel, etc.

- Existing measures to control the risk: list all measures that already mitigate the risk.  A standard operating procedure or local rules (eg for work with ionising radiation, lasers or biological hazards) will often address risks.  Some specific hazards may require detailed assessments in accordance with specific legislation (eg COSHH, DSEAR, manual handling, DSE work).   Where this is the case, and a detailed assessment has already been done in another format, the master risk assessment can simply cross-reference to other documentation.  For example, the activity might be use of a carcinogen, the hazard might be exposure to hazardous substances, the existing control measures might all be listed in a COSHH assessment.  Controls might also include use of qualified and/or experienced staff who are competent to carry out certain tasks.

- Risk Rating: Insert result – L, M or H

- L = trivial risk. Identifies low risk activities; it is unlikely that harm would arise under the controlled conditions listed, and even if exposure occurred, the injury would be relatively slight.

- M = adequately controlled, no further action necessary. The control measures currently in place offer adequate protection, and all legislative requirements have been met (and University policies complied with).

- H = high risk, actions required. The current control measures do not provide adequate protection. An action plan is required, which details the further control measures that must be implemented in order to bring the risks to an acceptable level

- Result : T, A, N or U:

T = trivial risk.  Use for very low risk activities to show that you have correctly identified a hazard, but that in the particular circumstances, the risk is insignificant.

A = adequately controlled, no further action necessary.   If your control measures lead you to conclude that the risk is low, and that all legislative requirements have been met (and University policies complied with), then insert A in this column.

N = not adequately controlled, actions required. Sometimes, particularly when setting up new procedures or adapting existing processes, the risk assessment might identify that the risk is high or medium when it is capable of being reduced by methods that are reasonably practicable.  In these cases, an action plan is required.  The plan should list the actions necessary, who they are to be carried out by, a date for completing the actions, and a signature box for the assessor to sign off that the action(s) has been satisfactorily completed.  Some action plans will be complex documents; others may be one or two actions that can be completed with a short timescale.

U = unable to decide. Further information required.  Use this designation if the assessor is unable to complete any of the boxes, for any reason.  Sometimes, additional information can be obtained readily (eg from equipment or chemicals suppliers, specialist University advisors) but sometimes detailed and prolonged enquiries might be required.  Eg is someone is moving a research programme from a research establishment overseas where health and safety legislation is very different from that in the UK.

For T and A results, the assessment is complete.

For N or U results, more work is required before the assessment can be signed off.

- Authorisation. Signature of principal investigator: the PI must sign and date the assessment, to confirm that they have considered and understand the experiment and the associated hazards, and that they are satisfied that all of the hazards have been identified and that the control measures to be followed will reduce the risks to acceptable levels.

- Declaration by researcher: the researcher must sign and date the assessment to confirm that they have read this Risk Assessment and understand the hazards and risks involved and will follow all of the safety procedures stated.

- Declaration by PI: the PI must countersign by each name to confirm that the researcher is competent to undertake the work, and that they are happy for the work to proceed.