Manchester Institute of Biotechnology  - Risk Assessment Form

| Date: 23/01/15 | Assessed by: Fiona Marriage | Validated by: Tanya Aspinall | Location: MIB |  | Review date: 22/01/16 |
| --- | --- | --- | --- | --- | --- |
| Task Bulk Storage of Flammable Materials in the MIB |

| Activity | Hazard | Person(s) in danger | Existing measures to control risk | Risk rating | Result |
| --- | --- | --- | --- | --- | --- |
| Bulk Storage of Flammable Materials | Risk of poisoning through inhalation / skin contact | Stores personnel | All Stores Personnel must be trained in the correct handling and storage of flammable material. They should have completed COSHH and risk assessments so that they are aware of the hazards associated with the handling of different specific flammable materials. The following items of PPE must be worn: Howie-style laboratory coat, BS EN374 compliant gloves (nitrile) and BS EN166 compliant eye protection (chemical splash proof safety glasses). A selection of safety glasses and goggles are available from MIB Stores; users are advised to visit Stores and select eye protection which fits well and is comfortable to use. Regular lab inspections monitor the wearing of PPE; users found not to be wearing PPE when the risk assessment states that it must be worn will be subject to the MIB compliance policy. Spills kit is available in case of spillage. The MIB has set procedures for the disposal of waste solvents (see MIB Safety Manual). All users must be aware of these procedures. No other method of disposal should be used. | low | A |
|  | Risk of fire | Staff and other building users | All Stores Personnel must be aware of the emergency procedures and location of all fire extinguishers and alarm points in/adjacent to the solvent warehouse and be trained in their use. All oxidising agents must be stored away from all flammable / combustible materials. Flammable materials must be stored in a designated flammable materials warehouse, which is compliant to current regulations. This site is to be a secure, cool, well ventilated, detached environment free from all sources of heat and ignition. No potential sources of sparks are to be taken into this area (Mobile Phones, Steel Shod Footwear etc). All storage areas are inspected on a regular basis. | High | A |
|  | Manual handling | Staff-could suffer damage to back if heavy/bulky items are incorrectly handled | Dedicated technical staff must be trained in correct manual handling techniques. Trolley must be used to transport heavy items. Flammable gases must be handled using manual handling gloves and cylinder trolleys. No cylinders will be issued from Stores unless users have an adequate trolley and appropriate safety footwear. Within the outside warehouse, vessels containing flammable liquids should be handled with one hand firmly around neck or handle and one hand on the underside of the vessel for support. All glass vessels of liquid from the outside warehouse should be transported in carriers designed for the job. No goods will be issued from Stores unless users have correct containers | low | A |

Authorisation by PI I confirm that I have considered and understand the experiment and the associated hazards. I am satisfied that all of the hazards have been identified and that the control measures to be followed will reduce the risks to acceptable levels. Print name: Signed: Date:

Declaration by researcher

I confirm that I have read this Risk Assessment and that I understand the hazards and risks involved and will follow all of the safety procedures stated. Where PPE has been identified as a control measure, I will ensure that it is worn.

Declaration by PI

I confirm that the researcher who has signed below is competent to undertake the work. My counter-signature indicates that I am happy for the work to proceed.

| Name (please print) | signed | PI countersignature | date |
| --- | --- | --- | --- |