Manchester Institute of Biotechnology - Risk Assessment

| Date: 23/01/15 | Assessed by: Michiyo SAKUMA | Validated by: Tanya Aspinall | Location: MIB |  | Review date: 22/01/16 |
| --- | --- | --- | --- | --- | --- |
| Task: Use of Cell Disruptor Lysis of bacterial cells with a Cell disruptor. Cell disruptor is based on the use of high pressure up to 40kpsi to force a sample through a small fixed orifice at high speed under controlled, contained and repeatable conditions. |

| Activity | Hazard | Person(s) in danger | Existing measures to control risk | Risk rating | Result |
| --- | --- | --- | --- | --- | --- |
| Use of cell disruptor | Bacterial aerosols | Staff and others in the lab | Staff trained by supervisor in safe use of cell disruptor. The following items of PPE must be worn: Howie-style laboratory coat, BS EN374 compliant gloves (nitrile) and BS EN166 compliant eye protection (chemical splash proof safety glasses). A selection of safety glasses and goggles are available from MIB Stores; users are advised to visit Stores and select eye protection which fits well and is comfortable to use. Regular lab inspections monitor the wearing of PPE; users found not to be wearing PPE when the risk assessment states that it must be worn will be subject to the MIB compliance policy. | Low | A |
|  | Water spillage / flooding | All lab staff | Ensure hose is securely fastened to cooling water supply tap or circulating chiller bath as appropriate. | Low | A |
|  | Mechanical hazard | Staff | All equipment and power supplies are safety tested and regularly maintained. | Low | A |
|  | Electrical hazard (maintenance) | Staff | Only suitably trained local users (currently M. Sakuma, R. Burke) may change the jet, target, high pressure seal and piston seal. Instructions for each operation may be found under the tooling menu on the main menu screen and MUST be adhered to, particularly with regard to electrical isolation. Any other maintenance operations must be undertaken by Constant Systems staff only. | Low | A |
|  | Electrical hazard - risk of electric shock | Staff | All equipment and power supplies are safety tested and regularly maintained. | Low | A |

Authorisation by PI I confirm that I have considered and understand the experiment and the associated hazards. I am satisfied that all of the hazards have been identified and that the control measures to be followed will reduce the risks to acceptable levels. Print name: Signed: Date:

Declaration by researcher

I confirm that I have read this Risk Assessment and that I understand the hazards and risks involved and will follow all of the safety procedures stated. Where PPE has been identified as a control measure, I will ensure that it is worn.

Declaration by PI

I confirm that the researcher who has signed below is competent to undertake the work. My counter-signature indicates that I am happy for the work to proceed.

| Name (please print) | signed | PI countersignature | date |
| --- | --- | --- | --- |