Manchester Institute of Biotechnology - Risk Assessment

| Date: | Assessed by: | Validated by: | Location: MIB | Review date: |
| --- | --- | --- | --- | --- |

Task: Analysis of chemically fixed cancer cells (different types of cancers will be studied) on MirrIR and CaF2 slides obtained from the Paterson Institute and Christie hospital in Didsbury with a Fourier Transform Infrared Imaging instrument located in room 1.064.

| Activity | Hazard | Person(s) in danger | Existing measures to control risk | Risk rating | Result |
| --- | --- | --- | --- | --- | --- |
| Cooling down of the FTIR imaging instrument with Liquid Nitrogen (up to 1L) | Release of liquid nitrogen-risk of asphyxiation | Members of Gardner lab working with such samples | All staff must be trained in correct handling and transport of liquid nitrogen. They must read risk assessments so that they are aware of the hazards associated with the handling of liquid nitrogen. Oxygen monitors and alarms are present in the room and are tested regularly to ensure they are functional. Warning signs and emergency advice are prominently displayed. No personnel to enter the room when oxygen alarm sounds. Staff to evacuate room when alarm sound continuously. | Low | A |
|  | Release of liquid nitrogen- risk of frostbite/cold burns | Members of Gardner lab working with such samples | All staff who handle/use liquid nitrogen must have attended a chemical safety course which details the risks associated with liquid nitrogen, and what to do in case of a burn injury. Protective clothing (lab coat, thermal gloves and glasses) are available and must be worn. Avoid exposing skin to liquefied gas. | Low | A |
| Handling of MirrIR and CaF2 slides with fixed cells | Possible broken slides-risk of cuts and grazes | Members of Gardner lab working with such samples | Tweezers are available in the lab to pick up the slides. | Low | T |
| Handling of MirrIR and CaF2 slides with fixed cells | Possible biological hazard | Members of Gardner lab working with such samples | The cell samples used are chemically fixed to the slides, which kills the cells. Therefore, there is no biological hazard associated with handling such samples, as the samples do not contain any living biological material. | Low | T |
| Handling of MirrIR and CaF2 slides with fixed cells | N/A | Members of Gardner lab working with such samples | Gloves will be worn to handle the slides with the fixed cells. | Low | T |

Authorisation by PI I confirm that I have considered and understand the experiment and the associated hazards. I am satisfied that all of the hazards have been identified and that the control measures to be followed will reduce the risks to acceptable levels. Print name: Signed: Date:

Declaration by researcher

I confirm that I have read this Risk Assessment and that I understand the hazards and risks involved and will follow all of the safety procedures stated.

Declaration by PI

I confirm that the researcher who has signed below is competent to undertake the work. My counter-signature indicates that I am happy for the work to proceed.

| Name (please print) | signed | PI countersignature | date |
| --- | --- | --- | --- |