Manchester Interdisciplinary Biocentre  - Risk Assessment Form

| Date: 27/01/15 | Assessed by: Mr. R. Spiess | Validated by: Tanya Aspinall | Location: MIB | Review date: 27/01/16 |
| --- | --- | --- | --- | --- |

| Activity | Hazard | Person(s) in danger | Existing measures to control risk | Risk rating | Result |
| --- | --- | --- | --- | --- | --- |
| Gas chromatography separation | Manual handling | Staff and maintenance engineer | The MS is heavy and requires assistance to move; All staff are trained in correct manual handling techniques, and in the use of the MS, by the EO responsible for the equipment. All work must be booked in using the logbooks provided. | low | A |
|  | Solvents |  | All Solvents used have COSHH forms, which must be read and signed before beginning work, and the control measures identified must be followed. The following items of PPE must be worn when handling solvents: Howie-style laboratory coat, BS EN374 compliant gloves (nitrile) and BS EN166 compliant eye protection (chemical splash proof safety glasses). A selection of safety glasses and goggles are available from MIB Stores; users are advised to visit Stores and select eye protection which fits well and is comfortable to use. Regular lab inspections monitor the wearing of PPE; users found not to be wearing PPE when the risk assessment states that it must be worn will be subject to the MIB compliance policy. | low | A |
|  | Moving parts | Staff | Auto-sampler moves during routine operation. Do not obstruct arm or rotating sample holder. | Low | A |
|  | Electrical hazard – risk of shock | staff | During training by supervisor, all users are made aware of potential risks from electric shocks. All equipment is annually tested (PA testing). Equipment with out of date, failed or untested labels are not be used until retested. Any obvious danger, sparks/damaged cables are reported immediately to technical staff and the equipment not used or switched off if in use No panels are removed (unless specifically trained to do so) | low | A |
|  | Sharp parts on equipment – risk of cuts | Staff and maintenance engineer | Many areas of the source and probe contain sharp items. These are normally protected by covers. Do not remove these without specific training. When handling fused silica columns take great care. This is a brittle material with sharp fractures. Use a specific silica cutting tool | low | A |
|  | Hot surfaces – risk of burns | staff | The injection port, GC oven and other areas are held at high temperature. Do not remove safety guards to access these areas until they have cooled. | low | A |
| Cleaning / servicing MS |  | Staff and maintenance engineer | No PPE is required for normal operation. When cleaning or servicing then BS EN374 compliant gloves (nitrile) and BS EN166 compliant eye protection (chemical splash proof safety glasses) are appropriate for many operations. In these cases a Howie-style laboratory coat must also be worn. | low | A |

Authorisation by Facility Manager I confirm that I have considered and understand the experiment and the associated hazards. I am satisfied that all of the hazards have been identified and that the control measures to be followed will reduce the risks to acceptable levels. Print name: Signed: Date:

Declaration by researcher

I confirm that I have read this Risk Assessment and that I understand the hazards and risks involved and will follow all of the safety procedures stated. Where PPE has been identified as a control measure, I will ensure that it is worn.

Declaration by Facility Manager

I confirm that the researcher who has signed below is competent to undertake routine unsupervised running of samples. My counter-signature indicates that I am happy for the work to proceed.

| Name (please print) | signed | Grant Code | Facility Manager signature | date |
| --- | --- | --- | --- | --- |