Manchester Institute of Biotechnology - Risk Assessment Form

| Date: 25/02/15 | Assessed by: Rebecca Davey | Validated by: Christopher Blanford | Location: Manchester Institute for Biotechnology | Assessment ref no: CFB 14 | Review date: 24/02/16 |
| --- | --- | --- | --- | --- | --- |
| Task / premises: Ultrasonic bath for graphene synthesis Related documents: see COSHH assessments for graphene suspensions |

| Activity | Hazard | Person(s) in danger | Existing measures to control risk | Risk rating | Result |
| --- | --- | --- | --- | --- | --- |
| Ultrasonic bath for graphene synthesis | Ultrasound (kHz) | User, persons in close proximity | Avoid skin contact with water during operation. Always use bath with sufficient water to prevent damage to the bath and reduce noise. | Low | A |
|  | Electric shock | User, persons in close proximity | Ensure equipment is PAT tested Fill and empty the bath using the hoses provided. | Low | A |
|  | Fumes from solvents | User, persons in close proximity | Fill bath with water. Solvents in a sealed container placed in the water. Ultrasonic bath must be used inside a fume hood | Low | A |
|  | Noise (nuisance) | User, persons in close proximity | Sound baffling and testing to ensure noise is below 80 dB to be compliant with HSE Control of Noise at Work Regulations 2005 | Low | A |
|  | Fire | User, persons in building | Bath used in fume hood or other ventilated areas to avoid build-up of solvent vapour Bath regularly tested to meet standards for electrical safety Nearby ignition sources removed | Low | A |
|  | Water leakage | Others in lab and on lower floors | Regular checks of hose integrity Clamps always used to secure hoses Checks on drains for blockages. | Low | A |

Authorisation by PI I confirm that I have considered and understand the experiment and the associated hazards. I am satisfied that all of the hazards have been identified and that the control measures to be followed will reduce the risks to acceptable levels. Print name: Christopher Blanford Signed: Date: 25 April 2014

Declaration by researcher

I confirm that I have read this Risk Assessment and that I understand the hazards and risks involved and will follow all of the safety procedures stated.

Declaration by PI

I confirm that the researcher who has signed below is competent to undertake the work. My counter-signature indicates that I am happy for the work to proceed.

| Name (please print) | signed | PI countersignature | date |
| --- | --- | --- | --- |