Manchester Institute of Biotechnology  - Risk Assessment Form

| Date: 27/02/2015 | Assessed by: Sandra Kennedy | Validated by: Tanya Aspinall | Location: G048, LG041 | Review date: 27/02/2015 |
| --- | --- | --- | --- | --- |

Task: Use of a hobby drill to extract powder from bone samples. This can involve drilling the surface of a bone sample to remove the outer layers or into the interior of a sample to remove bone powder, as well as drilling very small bone fragments.

| Activity | Hazard | Person(s) in danger | Existing measures to control risk | Risk rating | Result |
| --- | --- | --- | --- | --- | --- |
| Use of hobby drill | Drilling – risk of injury to hands and fingers | Staff | Staff must be trained in the proper use of the hobby drill for drilling bone samples. | M | A |
|  | Drilling – risk of bone shards breaking off | Staff | The following items of PPE must be worn: Howie-style laboratory coat, BS EN374 compliant gloves (nitrile) and BS EN166 compliant eye protection (chemical splash proof safety glasses). A selection of safety glasses and goggles are available from MIB Stores; users are advised to visit Stores and select eye protection which fits well and is comfortable to use. Regular lab inspections monitor the wearing of PPE; users found not to be wearing PPE when the risk assessment states that it must be worn will be subject to the MIB compliance policy. Alternatively, protective forensic suits must be worn. | L | A |
|  | Drilling – risk of loose clothing becoming caught | Staff | Lab coats (or protective forensic suits) must be worn at all times. Long hair must be tied back. | L | A |
|  | Electrical hazard – risk of electric shock | Staff | All equipment regularly maintained and PA tested annually. | L | A |
|  | Chemical hazard – cleaning of the drill bit | Staff | Lab coats (or protective forensic suits), safety glasses and gloves must be worn (detailed above). All chemicals used for cleaning (DNA Away, bleach and ethanol) must be COSHH assessed before use. Any identified control measures must be followed. | L | A |

Authorisation by PI I confirm that I have considered and understand the experiment and the associated hazards. I am satisfied that all of the hazards have been identified and that the control measures to be followed will reduce the risks to acceptable levels. Print name: Signed: Date:

Declaration by researcher

I confirm that I have read this Risk Assessment and that I understand the hazards and risks involved and will follow all of the safety procedures stated. Where PPE has been identified as a control measure, I will ensure that it is worn.

Declaration by PI

I confirm that the researcher who has signed below is competent to undertake the work. My counter-signature indicates that I am happy for the work to proceed.

| Name (please print) | signed | PI countersignature | date |
| --- | --- | --- | --- |