Manchester Institute of Biotechnology -  Risk Assessment

| Date: 27/01/15 | Assessed by: Mr. R. Spiess | Validated by: Tanya Aspinall | Location: MIB | Review date: 27/01/18 |
| --- | --- | --- | --- | --- |

Task: Use of mass spectrometry equipment (including LCMS).

| Activity | Hazard | Person(s) in danger | Existing measures to control risk | Risk rating | Result |
| --- | --- | --- | --- | --- | --- |
| Liquid chromatography separation | Manual handling | Staff and maintenance engineer | The MS is heavy and requires assistance to move; All staff are trained in correct manual handling techniques, and in the use of the MS, by the EO responsible for the equipment. All work must be booked in using the logbooks provided. | low | A |
|  | Solvents |  | All Solvents used have COSHH forms, which must be read and signed before beginning workAll identified control measures must be followed. The following items of PPE must be worn when handling solvents: Howie-style laboratory coat, BS EN374 compliant gloves (nitrile) and BS EN166 compliant eye protection (chemical splash proof safety glasses). A selection of safety glasses and goggles are available from MIB Stores; users are advised to visit Stores and select eye protection which fits well and is comfortable to use. Regular lab inspections monitor the wearing of PPE; users found not to be wearing PPE when the risk assessment states that it must be worn will be subject to the MIB compliance policy. | low | A |
|  | Electrical hazard – risk of shock | staff | During training by supervisor, all users are made aware of potential risks from electric shocks. All equipment is annually tested (PA testing). Equipment with out of date, failed or untested labels are not be used until retested. Any obvious danger, sparks/damaged cables are reported immediately to technical staff and the equipment not used or switched off if in use No panels are removed (unless specifically trained to do so) If using a conductive salt solution be aware that connected metallic items such as syringe needles could carry an electric charge. HV is present in many areas including the source. Ensure all panels are present or the supply switched off before accessing these areas. | low | A |
|  | Sharp parts on equipment – risk of cuts | Staff and maintenance engineer | Many areas of the source and probe contain sharp items. These are normally protected by covers. Do not remove these without specific training. When handling fused silica solvent lines take great care. This is a brittle material with sharp fractures. Use a specific silica cutting tool | low | A |
|  | Hot surfaces – risk of burns | staff | The source block and probe are heated. Do not remove safety guards to access these areas until they have cooled | low | A |
| Cleaning / servicing MS |  | Staff and maintenance engineer | When cleaning or servicing then safety glasses and gloves should be worn. | low | A |
| Routine operation | Moving parts | Users | No PPE is required for normal operation. Be aware and trained in the action of the autosampler. |  |  |

Authorisation by PI I confirm that I have considered and understand the experiment and the associated hazards. I am satisfied that all of the hazards have been identified and that the control measures to be followed will reduce the risks to acceptable levels. Print name: Signed: Date:

Declaration by researcher

I confirm that I have read this Risk Assessment and that I understand the hazards and risks involved and will follow all of the safety procedures stated. Where PPE has been identified as a control measure, I will ensure that it is worn.

Declaration by PI

I confirm that the researcher who has signed below is competent to undertake the work. My counter-signature indicates that I am happy for the work to proceed.

| Name (please print) | signed | PI countersignature | date |
| --- | --- | --- | --- |