Manchester Institute of Biotechnology  - Risk Assessment

| Date: | Assessed by: | Validated by: | Location: MIB | Review date: |
| --- | --- | --- | --- | --- |

Task: Cleaning up a broken mercury thermometer (glass) at room temperature The SOP for clear-up is attached - Grab & Go® Mercury Spill Kit NOTE – it is against MIB policy to use mercury thermometers, any in use should be replaced by alcohol ones which are available from MIB Stores. However we recognise that some labs have historical mercury thermometers – all intact ones must be disposed of via Hazardous Waste disposal. Broken ones must be cleaned up in accordance with this risk assessment. If in doubt, please contact the MIB Safety and Risk Manager.

| Activity | Hazard | Person(s) in danger | Existing measures to control risk | Risk rating | Result |
| --- | --- | --- | --- | --- | --- |
| Broken mercury thermometer | Release of Inorganic mercury | User and those in the vicinity, young persons and expectant mothers, and the environment Mercury may damage the unborn child. It is corrosive, toxic if inhaled and easily and absorbed through lungs, skin and alimentary system. It can cause burns Very toxic to aquatic life with long lasting effects Permissible exposure limit in 8 hours is 0.02 mg/m3 | Those not involved in the clean-up are expected to leave the area. Young people and expectant mothers must leave immediately. Users must contain the spill as much as possible before leaving the area to seek help (see SOP) The following items of PPE must be worn: Howie-style laboratory coat, BS EN374 compliant gloves (thick nitrile) and BS EN166 compliant eye protection (chemical splash proof safety glasses). A selection of safety glasses and goggles are available from MIB Stores; users are advised to visit Stores and select eye protection which fits well and is comfortable to use. Regular lab inspections monitor the wearing of PPE; users found not to be wearing PPE when the risk assessment states that it must be worn will be subject to the MIB compliance policy. The SOP for mercury clean up must be followed, and is attached to this document, along with the COSHH form for mercury and the clean up kit. | M | A |
|  | Broken glass | Glass – cuts and puncture wounds | Remove large glass fragments with blunt forceps and place in hazardous waste container with rest of clean up materials |  |  |
|  | Grab & Go® Mercury Spill Kit - Mercury Amalgamation Powder Mercury Indicator Powder | User – those in the vicinity, the environment kits do not contain any chemicals designed to alter the mercury’s toxicity or danger Mercury Indicator Powder causes serious eye damage; causes damage to organs through prolonged or repeated exposure and may cause skin irritation. Mercury Amalgamation Powder and Mercury Indicator Powder are very toxic to aquatic life with long lasting effects | The SOP is carefully followed All waste and clean-up materials are treated as hazardous waste The following items of PPE must be worn: Howie-style laboratory coat, BS EN374 compliant gloves (thick nitrile) and BS EN166 compliant eye protection (chemical splash proof safety glasses). A selection of safety glasses and goggles are available from MIB Stores; users are advised to visit Stores and select eye protection which fits well and is comfortable to use. Regular lab inspections monitor the wearing of PPE; users found not to be wearing PPE when the risk assessment states that it must be worn will be subject to the MIB compliance policy. The SOP for mercury clean up must be followed, and is attached to this document, along with the COSHH form for mercury and the clean up kit. | L | A |

Authorisation by PI I confirm that I have considered and understand the experiment and the associated hazards. I am satisfied that all of the hazards have been identified and that the control measures to be followed will reduce the risks to acceptable levels. Print name: Signed: Date:

Declaration by researcher

I confirm that I have read this Risk Assessment and that I understand the hazards and risks involved and will follow all of the safety procedures stated.

Declaration by PI

I confirm that the researcher who has signed below is competent to undertake the work. My counter-signature indicates that I am happy for the work to proceed.

| Name (please print) | signed | PI countersignature | date |
| --- | --- | --- | --- |

# Manchester Institute of Biotechnology - COSHH Assessment Form

# (Covering COSHH and DSEAR 2002)

| This assessment only addresses the risks from the named substance. Additional risk assessments may be required to control the risks from other hazards associated with this work/the procedures used. |
| --- |
| Assessor (print) | Principal Investigator/Supervisor |
| Assessment Date | Dates reviewed |
| Substance | Hazardous Properties | Quantity |
| Name of chemical | Mercury Thermometer containing elemental mercury CAS-No. 7439-97-6 | May damage the unborn child Can cause irreversible eye damage. Is easily absorbed through skin. Can be fatal if inhaled Very toxic to aquatic life with long lasting effects | NOTE: this COSHH risk assessment is for a broken mercury thermometer. Use of Mercury thermometers is prohibited in the MIB |
| Synonyms | Hg | Pictogram: Signal word: DANGER | Physical state Silver-white liquid |

| Hazards identified *Carcinogens, Mutagens and Reproductive Toxins (CMRs): Carcinogens are identified with R40, R45 or R49 risk phrases or H350, H350i or H351 hazard statements; Mutagens are identified with R46, R68 risk phrases, or H340, H341 hazard statements; Reproductive toxins are identified with R60, R61, R62 or R63 risk phrases, or H360, H361 hazard statements. It is important that CMRs are identified and a record of use is kept. Any exposure to CMRs must be reported immediately to your Supervisor and the MIB Safety and Risk Manager. Exposure is most likely to occur from a spillage or failure of the fume hood. |
| --- |
| Hazard (H) statements | H330 Fatal if inhaled. H360D May damage the unborn child. H372 Causes damage to organs through prolonged or repeated exposure. H410 Very toxic to aquatic life with long lasting effects. |
| Precautionary (P) statements | P201 Obtain special instructions before use. P260 Do not breathe dust/ fume/ gas/ mist/ vapours/ spray. P280 Wear protective gloves/ protective clothing/ eye protection/ face protection. P304 + P340 + P310 IF INHALED: Remove person to fresh air and keep comfortable for breathing. Immediately call a POISON CENTER or doctor/ physician. P308 + P313 IF exposed or concerned: Get medical advice/ attention. P403 + P233 Store in a well-ventilated place. Keep container tightly closed. |
| Other hazards | Broken glass |
| Workplace exposure limits | Permissible exposure limit in 8 hours = 0.02 mg/m3 |

| Emergency Procedures – All accidents must be reported |
| --- |
| Personal Injury |
| Eye contact | Flush eyes with water, use diphoterine eye wash. Seek urgent medical attention. |
| Skin contact | Wash off with soap and plenty of water, use diphoterine. Take victim immediately to hospital |
| Inhalation | If breathed in, move person into fresh air. Vapours may cause sore throat, coughing, pain, breathing difficulties Seek urgent medical attention |
| Ingestion | Rinse mouth with water and Take victim immediately to hospital |
| Accidental release measures i.e. spillages and gas release. If in doubt evacuate the area and raise the alarm. NEVER tackle a spill on your own |
| Contain with | MIB has chemical spills kits, which should be used in case of chemical spill. Soak up with inert absorbent material and dispose of as hazardous waste. Keep in suitable, closed containers for disposal. If you have spilt a significant amount, evacuate all personnel (including you) to a safe area. Get someone to stand outside the lab to prevent entry until the spill has been cleared up. Contact your PI and designated emergency contacts. |
| Fire Fighting Measures. If in doubt evacuate the area and raise the alarm NEVER tackle a fire on your own and only use fire extinguishers if trained to do so |
| Extinguishing media | Use water spray, alcohol-resistant foam, dry chemical or carbon dioxide |
| Special hazards arising | Mercury/mercury oxides. |

| METHODS OF PREVENTION OR CONTROL OF EXPOSURE (select all that apply by circling/ticking/highlighting the appropriate statement) |
| --- |
| 1. Engineering controls required total containment fume cupboard local exhaust ventilation blast screen | 2. Access control restricted to competent personnel special containment facility (give specific area): |
| 3. Special procedures Standard Operating Procedure (SOP) required for clean up of mercury spills Code of practice, local rules, etc | 4. Approved PPE ( Note: PPE is to be used as the ‘last resort’ when controlling exposure) EN374-3 compliant gloves (long thick nitrile) EN166 compliant eye protection (chemical splash-resistant goggles) Howie laboratory coat other PPE (specify) |

| Disposal Procedures (Give details of waste disposal procedure to be used) |
| --- |
| Are chemicals with risk phrases R50-R59 or hazard statements H400 – H413 (environmental hazards) involved? Yes If your substance is classed as an environmental hazard you must not let it enter the drainage system. |
| Disposal route | Waste is to be disposed of via MIB Stores, using the hazardous waste disposal procedure. |
| If hazardous, and requires disposal via Stores, please state EWC code | 06 04 04 |

| Handling and Storage requirements |
| --- |
| Training Requirements (List any specialised training requirements before work can begin) | All users must be trained in the use of this substance Inexperienced users must be supervised until competent |
| What will the chemical be used for? (insert title of experiment or experimental procedure) | Mercury thermometers are not permitted in the MIB. This assessment is for safe clean up of a mercury spill. |
| Who may be exposed? | Users and those in the vicinity Untrained users, those under 18 and lone workers may not use this product. Expectant and nursing mothers – Mercury may damage the unborn child |

ASSESSMENT OF RISK USING CONTROLS DETAILED ABOVE (are the hazards/risks suitably controlled, using the control measures detailed above? If not, state the further actions required, eg. Requirement for a standard operating procedure (SOP), etc). Low risk; The identified exposure prevention and control measures will reduce the risks to as low a level as reasonably practicable.

Authorisation by PI I confirm that I have considered and understand the chemical to be used and the associated hazards. I am satisfied that all of the hazards have been identified and that the control measures to be followed will reduce the risks to as low a level as reasonably practicable. Print name: Signed: Date:

Declaration by researcher

I confirm that I have read this COSHH Assessment and that I understand the hazards and risks involved and will follow all of the safety procedures stated.

Declaration by PI

I confirm that the researcher who has signed below is competent to undertake the work. My counter-signature indicates that I am happy for the work to proceed.

| Name (please print) | Signed | PI countersignature | date |
| --- | --- | --- | --- |

# Manchester Institute of Biotechnology - COSHH Assessment Form

# (Covering COSHH and DSEAR 2002)

| This assessment only addresses the risks from the named substance. Additional risk assessments may be required to control the risks from other hazards associated with this work/the procedures used. |
| --- |
| Assessor (print) | Principal Investigator/Supervisor |
| Assessment Date | Dates reviewed |
| Substance | Hazardous Properties | Quantity |
| Name of chemical | Grab & Go® Mercury Spill Kit 257g Mercsorb Mercury Amalgamation Powder 250g Mercury Indicator Powder | Mercury Amalgamation Powder and Mercury Indicator Powder are very toxic to aquatic life with long lasting effects Mercury Indicator Powder causes serious eye damage; causes damage to organs through prolonged or repeated exposure and may cause skin irritation. Exposure may aggravate those with pre-existing eye, skin, or respiratory conditions | 1 kit NOTE: MERCSORB® kits do not contain any chemicals designed to alter the mercury’s toxicity or danger. They are simply used to clean up mercury spills. Once used all components should be considered to be hazardous |
| Synonyms |  | Pictogram: Signal word: DANGER | Physical state Powders |

| Hazards identified *Carcinogens, Mutagens and Reproductive Toxins (CMRs): Carcinogens are identified with R40, R45 or R49 risk phrases or H350, H350i or H351 hazard statements; Mutagens are identified with R46, R68 risk phrases, or H340, H341 hazard statements; Reproductive toxins are identified with R60, R61, R62 or R63 risk phrases, or H360, H361 hazard statements. It is important that CMRs are identified and a record of use is kept. Any exposure to CMRs must be reported immediately to your Supervisor and the MIB Safety and Risk Manager. Exposure is most likely to occur from a spillage or failure of the fume hood. |
| --- |
| Hazard (H) statements | Mercury Amalgamation Powder H400 - Very toxic to aquatic life. H410 - Very toxic to aquatic life with long lasting effects Mercury Indicator Powder H302 - Harmful if swallowed H315 - Causes skin irritation H317 - May cause an allergic skin reaction H318 - Causes serious eye damage H372 - Causes damage to organs through prolonged or repeated exposure H400 - Very toxic to aquatic life H411 - Toxic to aquatic life with long lasting effects |
| Precautionary (P) statements | Mercury Indicator Powder P260 - Do not breathe dust. P264 - Wash hands, forearms, and exposed areas thoroughly after handling. P270 - Do not eat, drink or smoke when using this product. P272 - Contaminated work clothing must not be allowed out of the workplace. P273 - Avoid release to the environment. P280 - Wear eye protection, protective clothing, protective gloves. P301+P312 - IF SWALLOWED: Call a doctor, a POISON CENTER if you feel unwell. P302+P352 - IF ON SKIN: Wash with plenty of water. P305+P351+P338 - IF IN EYES: Rinse cautiously with water for several minutes. Remove contact lenses, if present and easy to do. Continue rinsing. P310 - Immediately call a doctor or POISON CENTER. P321 - Specific treatment (see Section 4). P330 - Rinse mouth. P332+P313 - If skin irritation occurs: Get medical advice/attention. P333+P313 - If skin irritation or rash occurs: Get medical advice/attention. P362 - Take off contaminated clothing and wash before reuse. P391 - Collect spillage. P501 - Dispose of contents/container in accordance with local, regional, national and international regulations. |
| Other hazards | Mercury Amalgamation Powder Forms combustible dust Mercury Indicator Powder Exposure may aggravate those with pre-existing eye, skin, or respiratory conditions Glass can cause serious cuts, puncture gloves and expose user |
| Workplace exposure limits | Mercury – exposure permissible in over 8 hours: 0.02 mg/m3 |

| Emergency Procedures – All accidents must be reported |
| --- |
| Personal Injury |
| Eye contact | Indicator powder Flush with copious amount of water and use diphoterine eye wash – keep washing / bathing the affected eye for at least 60 minutes. Seek urgent medical attentions (can take eye wash to A&E with you). |
| Skin contact | Rinse with water and use diphoterine for at least 15 minutes, seek medical attention if irritation develops and persists |
| Inhalation | Remove to fresh air and keep at rest in a position comfortable for breathing. Obtain medical attention if breathing difficulty persists. |
| Ingestion | Indicator powder Never give anything by mouth to an unconscious person. If you feel unwell, seek medical advice Amalgam powder Do NOT induce vomiting. Rinse mouth. Seek immediate medical attention – medics may need to call a POISON CENTER. |
| Accidental release measures i.e. spillages and gas release. If in doubt evacuate the area and raise the alarm. NEVER tackle a spill on your own |
| Contain with | MIB has chemical spills kits, which should be used in case of chemical spill. Soak up with inert absorbent material and dispose of as hazardous waste. Keep in suitable, closed containers for disposal. If you have spilt a significant amount, evacuate all personnel (including you) to a safe area. Get someone to stand outside the lab to prevent entry until the spill has been cleared up. Contact your PI and designated emergency contacts. |
| Fire Fighting Measures. If in doubt evacuate the area and raise the alarm NEVER tackle a fire on your own and only use fire extinguishers if trained to do so |
| Extinguishing media | Use extinguishing media appropriate for surrounding fire. |
| Special hazards arising | None listed |

| METHODS OF PREVENTION OR CONTROL OF EXPOSURE (select all that apply by circling/ticking/highlighting the appropriate statement) |
| --- |
| 1. Engineering controls required total containment fume cupboard local exhaust ventilation blast screen | 2. Access control restricted to competent personnel special containment facility (give specific area): |
| 3. Special procedures Standard Operating Procedure (SOP) required for clean up of mercury spills Code of practice, local rules, etc | 4. Approved PPE ( Note: PPE is to be used as the ‘last resort’ when controlling exposure) EN374-3 compliant gloves (long thick nitrile) EN166 compliant eye protection (chemical splash-resistant goggles) Howie laboratory coat other PPE (specify) |

| Disposal Procedures (Give details of waste disposal procedure to be used) |
| --- |
| Are chemicals with risk phrases R50-R59 or hazard statements H400 – H413 (environmental hazards) involved? Yes If your substance is classed as an environmental hazard you must not let it enter the drainage system. |
| Disposal route | Waste is to be disposed of via MIB Stores, using the hazardous waste disposal procedure. |
| If hazardous, and requires disposal via Stores, please state EWC code | Amalgamation powder: 06 13 03 Indicator powder: 16 05 06 Mercury: 06 04 04 |

| Handling and Storage requirements |
| --- |
| Conditions for safe storage and handling, including recommended temperature | Store away from direct sunlight in a cool dry area away from incompatible substances Avoid all contact with skin, eyes, or clothing. Avoid breathing dust Make sure all unnecessary personnel are out of the area Wear chemical splash proof goggles, gloves, a lab coat and overshoes Handle without creating dust Keep powder dry – wet vapour suppressor removes oxygen from air These chemicals are not designed to alter the mercury’s toxicity or danger. Handle accordingly. NOTE: Mercury is fatal if inhaled and may damage the unborn child Often thermometer breakage includes glass fragments – these can cut your hands, puncture gloves an expose user to mercury / clean up chemicals. Use blunt forceps to pick up large fragments and gently sweep up smaller fragments after the indicator step. |
| Conditions to avoid, including incompatible substances | Avoid Direct sunlight. Extremely high or low temperatures. Ignition sources. Incompatible materials Incompatible with Strong acids. Strong bases. Strong oxidizers |
| Training Requirements (List any specialised training requirements before work can begin) | All users must be trained in the use of this substance Inexperienced users must be supervised until competent |
| What will the chemical be used for? (insert title of experiment or experimental procedure) | The kit will be used to clear up mercury spills |
| Who may be exposed? | Users and those in the vicinity Untrained users, those under 18 and lone workers may not use this product. Expectant and nursing mothers should not use this kit – Mercury may damage the unborn child |

ASSESSMENT OF RISK USING CONTROLS DETAILED ABOVE (are the hazards/risks suitably controlled, using the control measures detailed above? If not, state the further actions required, eg. Requirement for a standard operating procedure (SOP), etc). Low risk; The identified exposure prevention and control measures will reduce the risks to as low a level as reasonably practicable.

Authorisation by PI I confirm that I have considered and understand the chemical to be used and the associated hazards. I am satisfied that all of the hazards have been identified and that the control measures to be followed will reduce the risks to as low a level as reasonably practicable. Print name: Signed: Date:

Declaration by researcher

I confirm that I have read this COSHH Assessment and that I understand the hazards and risks involved and will follow all of the safety procedures stated.

Declaration by PI

I confirm that the researcher who has signed below is competent to undertake the work. My counter-signature indicates that I am happy for the work to proceed.

| Name (please print) | Signed | PI countersignature | date |
| --- | --- | --- | --- |