Manchester Institute of Biotechnology -  Risk Assessment

| Date: Jan 2015 | Assessed by: Sandra Kennedy | Validated by: Tanya Aspinall | Location: MIB Labs |  | Review date: 2016 |
| --- | --- | --- | --- | --- | --- |
| Task Use of Microwave Ovens |

| Activity | Hazard | Person(s) in danger | Existing measures to control risk | Risk rating | Result |
| --- | --- | --- | --- | --- | --- |
| Use of Microwave Ovens | Burns from steam, hot metal, hot liquids, glassware | Staff | The following items of PPE must be worn: Howie-style laboratory coat, BS EN 407 compliant gloves (thermal protective gloves) and BS EN166 compliant eye protection (chemical splash proof safety glasses). A selection of safety glasses and goggles are available from MIB Stores; users are advised to visit Stores and select eye protection which fits well and is comfortable to use. Regular lab inspections monitor the wearing of PPE; users found not to be wearing PPE when the risk assessment states that it must be worn will be subject to the MIB compliance policy. | low | A |
|  | Explosion – due to over-tightened lids on bottles | Staff and others in close proximity | Staff trained in correct use of microwaves by supervisor, including the need to unscrew bottles (or there is a risk of explosion) and the non-use of metals/tin foil in the microwave. | low | A |
|  | Microwaves – if inadequate seal on door | Staff and others in close proximity | Annual testing of equipment | low | A |
|  | Electricity – risk of electric shock | staff | Annual PA testing of equipment | Low | A |

Authorisation by PI I confirm that I have considered and understand the experiment and the associated hazards. I am satisfied that all of the hazards have been identified and that the control measures to be followed will reduce the risks to acceptable levels. Print name: Signed: Date:

Declaration by researcher

I confirm that I have read this Risk Assessment and that I understand the hazards and risks involved and will follow all of the safety procedures stated. Where PPE has been identified as a control measure, I will ensure that it is worn.

Declaration by PI

I confirm that the researcher who has signed below is competent to undertake the work. My counter-signature indicates that I am happy for the work to proceed.

| Name (please print) | signed | PI countersignature | date |
| --- | --- | --- | --- |