Manchester Institute of Biotechnology  - Risk Assessment

| Date: Feb 2015 | Assessed by: Colin Levy | Validated by: Tanya Aspinall | Location: MIB LG027 | Review date: Feb 2016 |
| --- | --- | --- | --- | --- |

Task: Operation of the Phoenix Pipetting Robot

| Activity | Hazard | Person(s) in danger | Existing measures to control risk | Risk rating | Result |
| --- | --- | --- | --- | --- | --- |
| Use of electrical equipment (general). | Electric Shock | User | During training by supervisor, all users are made aware of potential risks from electric shocks. All users must have attended a basic health and safety course where part of the instruction covers risks from electric shocks and first aid procedures in the event of a shock. All equipment is annually tested (PAT testing). Equipment with out of date, failed or untested labels must not to be used until retested. Any obvious danger, sparks/damaged cables must be reported immediately to technical staff and the equipment not used or switched off if in use. Any faults associated with the equipment must be reported immediately to the person in charge of the laboratory. Unauthorised/untrained personnel must not attempt to dismantle any part of the equipment for any purpose. | L | T |
| Use of Phoenix to setup crystallogenesis plates | Moving machinery / Pinch Hazard | User | Pinch point labels are displayed on moving parts. Once the robot has been loaded users must not, under any circumstances, place hands into the robot operating area until the selected protocol has either deliberately paused or ended | L | T |
| Use of Crystallisation Screens | Chemical Hazard | User | Any chemicals imported to the Facility must have been previously assessed by the User in their home laboratory. COSHH records will be the responsibility of the User. Crystallisation screens utilised in the facility have full MSDS available in the Health and Safety file and users should be familiar with their contents. This is covered during facility induction. Any spills must be immediately cleaned up using appropriate PPE and the area made safe for future users. | L | T |

Authorisation by PI I confirm that I have considered and understand the experiment and the associated hazards. I am satisfied that all of the hazards have been identified and that the control measures to be followed will reduce the risks to acceptable levels. Print name: Signed: Date:

Declaration by researcher

I confirm that I have read this Risk Assessment and that I understand the hazards and risks involved and will follow all of the safety procedures stated.

Declaration by PI

I confirm that the researcher who has signed below is competent to undertake the work. My counter-signature indicates that I am happy for the work to proceed.

| Name (please print) | signed | PI countersignature | date |
| --- | --- | --- | --- |