MIB General Risk Assessment Form

| Date: 25/02/15 | Assessed by: Christopher Blanford | Validated by: Tanya Aspinall | Location: MIB second-floor chemistry laboratory |  | Review date: 24/02/16 |
| --- | --- | --- | --- | --- | --- |
| Task: Use of quartz crystal microbalance with a gas sparge (Also requires understanding and signoff on CFB 01: electrical (including potentiostats), CFB 07: transport and use of compressed gases.) |

| Activity | Hazard | Persons in danger | Existing measures to control risk | Risk rating | Result |
| --- | --- | --- | --- | --- | --- |
| Saturating solution feed to QCM with gas | Changes in local gas composition, e.g., oxygen enrichment/depletion, addition of flammable/explosive gas | User, those in vicinity, including non-scientific staff | All measures are in addition to those specified in the risk assessment “gas cylinders”. Gas flow rate should be kept to a minimum level. Typical levels are <1 litre/min. The bottle containing the solution to be sparged should have three holes, one each for: gas inlet, gas outlet, solution withdrawal. The bottle should be held fast, e.g., with a clamp. The gas outlet should be piped to a fume cupboard or exhaust snorkel. A device that cuts off gas flow in the event of a power failure should be installed, if one is available. Oxygen levels should be monitored for evidence of local enrichment or depletion, if a device is available. | LOW | A |
|  | “Blowpipe” effects: projectile injury | User, those in vicinity, including non-scientific staff | Tips or fixtures generally should not be attached to the end of the sparge hose. If tips must be attached, they should be fixed in place with appropriate adhesive or clamps. | LOW | A |
| Saturating solution feed to QCM with O2 or flammable gases | Creation of conditions in which likelihood or severity of explosions in increased | User, those in building, including non-scientific staff, occupants of neighbouring buildings | These measures are in addition to those above. Removal of potential fuels (e.g., solvents, paper, dust) and sources of ignition from within 0.5 m of any part of the gas delivery system outside a fume cupboard. | LOW | A |

Authorisation by PI I confirm that I have considered and understand the experiment and the associated hazards. I am satisfied that all of the hazards have been identified and that the control measures to be followed will reduce the risks to acceptable levels. Print name: Christopher Blanford Signed: Date:

Declaration by researcher

I confirm that I have read this Risk Assessment and that I understand the hazards and risks involved and will follow all of the safety procedures stated.

Declaration by PI

I confirm that the researcher who has signed below is competent to undertake the work. My counter-signature indicates that I am happy for the work to proceed.

| Name (please print) | signed | PI countersignature | date |
| --- | --- | --- | --- |