MIB General Risk Assessment Form

| Date: 25/02/15 | Assessed by: Kulveer Singh | Validated by: Christopher Blanford | Location: MIB second-floor chemistry laboratory |  | Review date: 24/02/16 |
| --- | --- | --- | --- | --- | --- |
| Task: Use of rotating disc electrode setup with gas purging (must be used in conjunction with the “gas cylinder” risk assessment) |

| Activity | Hazard | Persons in danger | Existing measures to control risk | Risk rating | Result |
| --- | --- | --- | --- | --- | --- |
| Saturating solution feed to rotating disc electrode setup | Changes in local gas composition, e.g., oxygen enrichment/depletion, addition of flammable/explosive gas | User, those in vicinity, including non-scientific staff | All measures are in addition to those specified in the “gas cylinder” risk assessment. Gas flow rate must be kept to a minimum level. Typical levels are <2 litre/min. Controlled using mass flow controller. The bottle containing the solution to be sparged should have three holes, one each for: gas inlet, gas outlet, solution withdrawal. The bottle should be held fast, e.g., with a clamp. The gas outlet must be piped to a fume cupboard or exhaust snorkel. A device that cuts off gas flow in the event of a power failure must be installed, if one is available. Oxygen levels are monitored for evidence of local enrichment or depletion. | LOW | A |
|  | “Blowpipe” effects: projectile injury | User, those in vicinity, including non-scientific staff | Tips or fixtures must not normally be attached to the end of the sparge hose. If tips must be attached, they must be fixed in place with appropriate adhesive or clamps. | LOW | A |
| Saturating solution feed to RDE with O2 or flammable gases | Creation of conditions in which likelihood or severity of explosions in increased | User, those in building, including non-scientific staff, occupants of neighbouring buildings | These measures are in addition to those above. Removal of potential fuels (e.g., solvents, paper, dust) and sources of ignition from within 0.5 m of any part of the gas delivery system outside a fume cupboard. | LOW | A |

Authorisation by PI I confirm that I have considered and understand the experiment and the associated hazards. I am satisfied that all of the hazards have been identified and that the control measures to be followed will reduce the risks to acceptable levels. Print name: Christopher Blanford Signed: Date:

Declaration by researcher

I confirm that I have read this Risk Assessment and that I understand the hazards and risks involved and will follow all of the safety procedures stated.

Declaration by PI

I confirm that the researcher who has signed below is competent to undertake the work. My counter-signature indicates that I am happy for the work to proceed.

| Name (please print) | signed | PI countersignature | date |
| --- | --- | --- | --- |