Manchester Institute of Biotechnology  - Risk Assessment

| Date: 05/02/2015 | Assessed by: Tom Hodgkinson | Validated by: Tanya Aspinall | Location: MIB Room 2.058 |  | Review date: 05/02/2016 |
| --- | --- | --- | --- | --- | --- |
| Task Use of TissueLyser. Homogenising tissue samples ready for DNA, RNA or protein extraction. |

| Activity | Hazard | Person(s) in danger | Existing measures to control risk | Risk rating | Result |
| --- | --- | --- | --- | --- | --- |
| Use of Homogeniser Equipment. | Biological Hazard – Tissue Biopsies | Staff | All biological work must be risk assessed before the work begins. Biological material must be treated as potentially hazardous. All personnel working with biological samples are recommended to have Hepatitis B vaccination (available from Occupational Health). | low | A |
|  | Chemical Hazard –Trizol (inhalation or touch | Staff | A COSHH assessment (including information on what to do in case of accident) was carried out for Trizol, and must be read and signed before the work begins. The following items of PPE must be worn when handling Trizol solutions: Howie-style laboratory coat, BS EN374 compliant gloves (nitrile) and BS EN166 compliant eye protection (chemical splash proof safety glasses). A selection of safety glasses and goggles are available from MIB Stores; users are advised to visit Stores and select eye protection which fits well and is comfortable to use. Regular lab inspections monitor the wearing of PPE; users found not to be wearing PPE when the risk assessment states that it must be worn will be subject to the MIB compliance policy. | low | A |
|  | Trailing electrical leads – risk of slips/trips | Staff and others in lab | All excess leads are coiled and taped to minimise the risk of slip/trips. | low | A |
| Sterilising Metal Ball Bearings | Burn Hazard – Sterilising ball bearings by flaming in ethanol | Staff | A COSSH assessment (including information on what to do in case of accident) was carried out for ethanol, and must be read and signed before the work begins. Metal ball bearings must be sterilised in a heat resistant Petri dish using a small amount of ethanol. Igniting the ethanol must be performed well away from any flammable chemicals/solvents. PPE (as detailed above) must be worn at all times when handling ethanol. | low | A |
|  | Broken glass – risk of cuts from broken glass Petri dishes | Staff | All glass Petri dishes are regularly checked for damage, and broken/cracked/chipped dishes are discarded into the dedicated glass bins for disposal. | low | A |

Authorisation by PI I confirm that I have considered and understand the experiment and the associated hazards. I am satisfied that all of the hazards have been identified and that the control measures to be followed will reduce the risks to acceptable levels. Print name: Signed: Date:

Declaration by researcher

I confirm that I have read this Risk Assessment and that I understand the hazards and risks involved and will follow all of the safety procedures stated.

Declaration by PI

I confirm that the researcher who has signed below is competent to undertake the work. My counter-signature indicates that I am happy for the work to proceed.

| Name (please print) | signed | PI countersignature | date |
| --- | --- | --- | --- |