Manchester Institute of Biotechnology  - Risk Assessment

| Date: 29/01/15 | Assessed by: Fiona Marriage | Validated by: Tanya Aspinall | Location: MIB |  | Review date: 29/01/16 |
| --- | --- | --- | --- | --- | --- |
| Task Use of typhoon machine |

| Activity | Hazard | Person(s) in danger | Existing measures to control risk | Risk rating | Result |
| --- | --- | --- | --- | --- | --- |
| Use of typhoon machine | Manual handling | Staff and maintenance engineer | The typhoon machine is heavy and requires assistance to move; All staff are trained in correct manual handling techniques. | low | A |
|  | Electrical hazard – risk of shock | staff | During training by supervisor, all users are made aware of potential risks from electric shocks. All equipment is annually tested (PA testing). Equipment with out of date, failed or untested labels are not be used until retested. Any obvious danger, sparks/damaged cables are reported immediately to technical staff and the equipment not used or switched off if in use No panels are removed (unless specifically trained to do so) | low | A |
|  | Laser – risk of burns | staff | All guards must be in place before starting the operation All users must be fully trained in using the equipment (from their supervisor or the EO responsible for the equipment) Regular maintenance will ensure that laser hazards are confined and pose no danger to health. Typhoon machine to be fully maintained in accordance with manufacturer’s instructions. Servicing and repair to be carried out by the manufacturer or by suitably qualified personnel. | medium | A |
|  | Chemical hazard | staff | In order to prevent contamination of the glass plate, all gels must be securely double wrapped in saran to ensure no leakage can occur. Glass plate is to be cleaned after use, using water and tissue to ensure glass plate is left in a dry condition. The following items of PPE must be worn: Howie-style laboratory coat and BS EN374 compliant gloves (nitrile). A selection of safety glasses and goggles are available from MIB Stores; users are advised to visit Stores and select eye protection which fits well and is comfortable to use. Regular lab inspections monitor the wearing of PPE; users found not to be wearing PPE when the risk assessment states that it must be worn will be subject to the MIB compliance policy | medium | A |

Authorisation by PI I confirm that I have considered and understand the experiment and the associated hazards. I am satisfied that all of the hazards have been identified and that the control measures to be followed will reduce the risks to acceptable levels. Print name: Signed: Date:

Declaration by researcher

I confirm that I have read this Risk Assessment and that I understand the hazards and risks involved and will follow all of the safety procedures stated. Where PPE has been identified as a control measure, I will ensure that it is worn.

Declaration by PI

I confirm that the researcher who has signed below is competent to undertake the work. My counter-signature indicates that I am happy for the work to proceed.

| Name (please print) | signed | PI countersignature | date |
| --- | --- | --- | --- |