Manchester Institute of Biotechnology  - Risk Assessment

| Date: 21/09/16 | Assessed by: Beenish Siddique | Validated by: Prof Alberto Saiani | Location: MIB first floor Room 1.052 (fume hood) | Review date: 21/9/2017 |
| --- | --- | --- | --- | --- |

Task: Use of UV lamp for the polymerisation of polymer to prepare hydrogels in the fume cupboard

| Activity | Hazard | Person(s) in danger | Existing measures to control risk | Risk rating | Result |
| --- | --- | --- | --- | --- | --- |
| Use of UV lamp (UVL-28 EL Series UV lamp 8 watt/ 365nm/P/N 9-0248-02 0.32 AMPS/230v-50 | Electricity-risk of electric shock | Users + Anyone nearby | Annual PA testing of equipment by a qualified electrician. Pre-use inspection of equipment. Any defects will be reported immediately and the equipment will not be used. | Low | A |
| Use of UV lamp (UVL-28 EL Series UV lamp 8 watt/ 365nm/P/N 9-0248-02 0.32 AMPS/230v-50 | Radiation/ Ultraviolet (UV) radiation can cause damage to unprotected eyes and skin | Users + Anyone nearby | UV-protective eyewear must be worn. When operating UV-lamp always wear other personal protective equipment (face protection, suitable gloves and a lab coat) Put Ultraviolet caution sign on the safety fume cupboard Ensure that fume cupboard sash is covered with the tin foil and black paper to reduce amount of UV escaping from the fume cupboard. | Low | A |

Authorisation by PI I confirm that I have considered and understand the experiment and the associated hazards. I am satisfied that all of the hazards have been identified and that the control measures to be followed will reduce the risks to acceptable levels. Print name: Prof Alberto Saiani Signed: Date: 21/09/2016

Declaration by researcher

I confirm that I have read this Risk Assessment and that I understand the hazards and risks involved and will follow all of the safety procedures stated.

Declaration by PI

I confirm that the researcher who has signed below is competent to undertake the work. My counter-signature indicates that I am happy for the work to proceed.

| Name (please print) | signed | PI countersignature | date |
| --- | --- | --- | --- |