Manchester Institute of Biotechnology  - Risk Assessment

| Date: 13/4/17 | Assessed by: Natalie Parsons | Validated by: Tanya Aspinall | Location: MIB Lab Floor 1 | Review date: 12/4/18 |
| --- | --- | --- | --- | --- |

Task: Use of pH meters

| Activity | Hazard | Person(s) in danger | Existing measures to control risk | Risk rating | Result |
| --- | --- | --- | --- | --- | --- |
| Use of pH meters | Chemical | User and others working in the lab | pH meters are to be used only by trained personnel and in accordance with the manufacturers operating instructions. Users must be supervised until competent to work alone. Spillages must be cleared up immediately and decontaminated appropriately. Strong acids/alkalis are used to pH solutions. The following items of PPE must be worn when handling these solutions: Howie-style laboratory coat, BS EN374 compliant gloves (nitrile) and BS EN166 compliant eye protection (chemical splash proof safety glasses). A selection of safety glasses and goggles are available from MIB Stores; users are advised to visit Stores and select eye protection which fits well and is comfortable to use. Regular lab inspections monitor the wearing of PPE; users found not to be wearing PPE when the risk assessment states that it must be worn will be subject to the MIB compliance policy. All chemicals used with the pH meter must be COSHH assessed. The relevant COSHH forms must be read and signed to confirm understanding and that the control measures will be followed. | L | A |
| Use of pH meter | Electricity | User | All staff must be trained by their supervisor in the safe use of the equipment and made aware of the hazards and correct procedures to follow. Annual PA testing of the equipment must be carried out by a qualified electrician. Do not use equipment if the safety testing of the equipment is overdue. | L | A |

Authorisation by PI I confirm that I have considered and understand the experiment and the associated hazards. I am satisfied that all of the hazards have been identified and that the control measures to be followed will reduce the risks to acceptable levels. Print name: Signed: Date:

Declaration by researcher

I confirm that I have read this Risk Assessment and that I understand the hazards and risks involved and will follow all of the safety procedures stated. Where PPE has been identified as a control measure, I will ensure that it is worn.

Declaration by PI

I confirm that the researcher who has signed below is competent to undertake the work. My counter-signature indicates that I am happy for the work to proceed.

| Name (please print) | signed | PI countersignature | date |
| --- | --- | --- | --- |